NetworkÐtoÐNetwork Technical Interface
for Local Interconnection

NP QueryÐResponse Network Capability

Version 1.0

Document History

| Version | Date | Reason for Issue |
| --- | --- | --- |
| 0.1 | 1997 07 22 | Initial issue |
| 0.2 | 1997 09 16 | Incorporate reference to Message Set B |
| 1.0 | 1997 10 30 | Final version for interconnection |

ACKNOWLEDGMENT

In order to remain consistent with accepted industry standards and definitions, substantial portions of this document are based on publications of the American National Standards Institute (ANSI), and other industry sources as noted herein. The documents referred to herein shall be interpreted in the context of the Canadian regulatory framework.

Table of Contents

1. Introduction

1.1. Purpose

1.2. Scope

2. Interface

2.1. MTP

2.2. SCCP

2.3. TCAP

2.4. NP Query–Response Application Service Elements

3. References

4. Acronyms

Introduction

Purpose

This document is one of a series specifying the technical requirements for the interface(s) between local exchange carrier (LEC) networks. Within this document, the term Òlocal exchange carrierÓ is used to equivalently identify either an Incumbent Local Exchange Carrier (ILEC) or a Competitive Local Exchange Carrier (CLEC).

Conformance to the requirements specified in this document is intended to ensure interworking. In this context we define interworking as the ability of an end user to invoke a telecommunications service with end-to-end characteristics that depend on the transfer of signalling information across the interconnected local carrier networks. Adherence to these requirements should ensure that the interconnecting local carrier networks have equivalent capabilities for providing the telecommunications services defined here.

Recognizing that a single interconnection point may be able to support multiple independent telecommunications services, these technical interface specifications are similarly structured as a collection of independent interface specifications. Individual interface specifications may be used, either singly or in combination, to address the business and regulatory requirements of an interconnection between a pair of local carrier networks.

This technical interface specification describes the telecommunications service enabled by the interface in generic terms only. The specific characteristics of a telecommunications service offered by a local carrier are the responsibility of that individual local carrier and need conform to the generic description in these documents only to the extent required for internetwork interoperability of the service.

Description of a service and its associated technical interface in this document does not constitute a requirement for a local carrier to offer the interface to interconnectors. Individual local carriers are responsible for determining the services and interfaces that they will offer in order to meet their business needs and regulatory requirements.

A local carrier may offer additional services, not impacting the networkÐtoÐnetwork interface, to its subscribers. Such services are outside the scope of the technical interface(s) described in this series of documents.

Scope

The NP QueryÐResponse Network Capability describes an interface between two network elements, the query node and a number portability (NP) database. The interface enables the query node to request the NP database to provide a routing number corresponding to a given portable number. The interface described here is based on ANSI T1.660Ð1997, American National Standard for TelecommunicationsÑSignalling System Number 7 (SS7)ÑCall Completion to a Portable Number. The NP QueryÐResponse Network Capability is specified in Annex A of ANSI T1.660.

ANSI T1.660 uses the term Ònetwork routing number (NRN)Ó to refer to the routing number returned by the database. In other contexts this same number is referred to as the Òlocation routing number (LRN).Ó For the purpose of this specification, these two terms should be considered to be synonymous. In a number portability environment the NRN identifies the switch currently serving the portable number given in the query.

Interface

The following sections deal respectively with Message Transfer Part (MTP), Signalling Connection Control Part (SCCP), Transaction Capabilities (TCAP) and NP QueryÐResponse application specific options of the interface for obtaining the NRN from the NP database.

Since the MTP options for the interface are common to all applications using a local carrier network interconnection, their description is mainly by reference to the relevant sections of NetworkÐtoÐNetwork Technical Interface for Local Interconnection: Basic SS7 Call Control. (Hereafter referred to as the Basic Call Specification).

For other protocol parts, the description is in a tabular form with each row of the table corresponding to a particular capability of the protocol that affects the interface between local carrier networks for the NP QueryÐResponse network capability. The table columns have the following meanings:

Status gives the status of use of a protocol capability. Status has one of the following values:

M
Mandatory; support for the protocol capability is required at the interface between interconnecting local networks.

OO
Originating Option; support for the use of the protocol option is mandatory at the interface between interconnecting local networks. The originating network for a message determines whether or not to invoke the option for the message.

OT
Terminating Option; the network receiving a message determines its support for the protocol option. Use of the protocol option at an interface between interconnecting local networks is subject to agreement by the network receiving a message which invokes the option.

N/A
Not applicable or not available; the protocol option is not available for use across the interface between interconnecting local networks.

V
Value; the option specifies a particular value or set of values permitted for a parameter of the protocol. In this case the comments column specifies the value or value set.

Description is a short title for the protocol option.

Comments expand on the meaning of the protocol feature and, when the option identifies the permitted set of values for a protocol parameter, actually lists the allowed value or value set.

It should be emphasized that the tabular specifications identify only the use of particular protocol capabilities of the NP QueryÐResponse network capability at the local carrier interface and shall be interpreted within the framework established by the ANSI Standards for the protocol parts in question and the NP QueryÐResponse Network Capability.

MTP

At the MTP level the NP QueryÐResponse network capability uses the same internetwork facilities (signalling links) in the same configurations (AÐlink or DÐlink), as the basic call control interface. Figures 1a and 1b provide schematics of some typical interconnections applicable for NP QueryÐResponse corresponding to Figure 1a/Basic Call Specificationand Figure 1b/Basic Call Specification respectively.

Figure 1a Interconnection SchematicÑInterconnection on AÐlinks

Figure 1b Interconnection SchematicÑInterconnection on DÐlinks

ANSI T1.111 provides the basic definition of the MTP. The MTPÐrelated requirements in Section 2.3/Basic Call Specification, General Characteristics of the Interface, and Section 2.4/Basic Call Specification, Message Transfer Part, also apply to the use of the interface for NP QueryÐResponse.

SCCP

Table 1 specifies the use of SCCP protocol capabilities to support the NP QueryÐResponse network capability. ANSI T1.112 provides the basic definition of the SCCP.

Table 1 SCCP Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| M | Protocol Class 0 | SCCP protocol class 0 procedures provide for basic connectionless data transmission without sequence control |
| N/A | Protocol Class 1 | Sequenced connectionless data transmission |
| N/A | Protocol Class 2 | Basic connectionÐoriented data transmission |
| N/A | Protocol Class 3 | ConnectionÐoriented data transmission with flow control |
| N/A | Extended CL Messages | XUDT and XUDTS messages are allowable |
| OO | Message return on error | Return of a UDTS message in response to a UDT message that cannot be delivered because of a protocol error or network failure |
| OO | Global Title Called Party Address | Called Party Address parameter may contain a global title address |
| M | Point code, SSN Called Party Address | Called Party Address parameter may contain an address in point code, SSN format (note 1) |
| V | Called party address/ translation group | Translation group 11, as described in T1.112.3, Appendix B (note 2) |
| N/A | Global Title Calling Party Address | Calling Party Address parameter may contain a global title address |
| M | Point code, SSN Calling Party Address | Calling Party Address parameter may contain an address in point code, SSN format (note 1) |
| N/A | Calling party address/ translation group |

Table 1(continued) SCCP Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| N/A | International format address indicator and address | Bit 8 of the address indicator in calling and called party address parameters coded 1 |
| M | National format address indicator and address |
|  | V | Global Title Indicator Value | When using a global title address, the Global Title Indicator (GTI) takes value 2(00102) |
| N/A | Intermediate Signalling Network Identification (ISNI) Routing | ISNI allows for the specification of an SS7 network or networks used to route a message between its source and destination networks. |

Notes:

When an SCCP calling or called party address is in the point code + SSN form, the point code is normally transferred in the signalling label (OPC or DPC fields respectively). The exception to this is the case of a Calling Party Address when global title routing is in use. (See T1.112.3 ¤¤3.4Ð3.5)

The assignment of translation type 11 for this purpose by the SCCP subÐworking group of T1S1.3 took place after balloting of ANSI T1.112Ð1996. The assignment is documented in the Meeting Report of the June 1996 meeting of T1S1.3. This meeting report is available from ATIS as document number T1S1.3/96Ð195.

TCAP

Table 2 specifies the use of TCAP protocol capabilities to support the NP QueryÐResponse network capability. ANSI T1.114 provides the basic definition of TCAP.

Table 2 TCAP Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| M | Query, response messages | Support for sending and receiving these TCAP message types |
| N/A | Conversation message | Support for sending and receiving this TCAP message type |
| N/A | Unidirectional message | Support for sending and receiving this TCAP message type |
| OT | Abort message | Support for sending and receiving this TCAP message type |

NP QueryÐResponse Application Service Elements

The protocol between the query node and NP database is asymmetric. An ASE at the NP database, the DB ASE, acts as the supplier of a service to an ASE at the query node, the QÊASE. For the protocols defined in ANSI T1.660 Annex A each of these ASEs invokes an operation that the other ASE executes. ANSI T1.660 Annex A defines two possible protocols that may be used between the query node and the NP database. An NP SCP may support either one or both of these protocols. The following LEC interface specification however describes only one of these protocols, namely Message Set A, based on the Advanced Intelligent Network protocols developed by Bellcore. Tables 3–4 specify the use of protocol capabilities by the Q and DB Application Service Elements.

Where the capability described is a limit value for a timers used by an ASE to ensure correct operation of the service the specification gives either a lower bound (e.g. min( T1 )) or an upper bound (e. g. max( T2 )) on the initial setting of the timer. A LEC network may choose to use values greater than a lower bound or less than an upper bound.

This section also specifies internetwork addressing and routing requirements for the different types of TCAP messages generated by the ASEs. These requirements apply to messages transferred across an SPOI toward another local carrier signalling network. That is the requirements apply to messages transferred:

From Query Node to Nb in the configuration of Figure 1a.

In either direction between Na and Nb in the configuration of Figure 1b.

Messages transferred across an SPOI toward an individual signalling point, i.e. from Nb to Query Node in the configuration of Figure 1a, always route using the destination point code and SSN.

Table 3 Q Application Service Element Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| M | Global title internetwork addressing of query messages | TCAP messages of this type specify Òroute on global titleÓ in the SCCP Called Party Address. |
| N/A | Point code, SSN internetwork addressing of query messages | TCAP messages of this type specify Òroute on point code + SSNÓ in the SCCP Called Party Address |
| N/A | Global title internetwork addressing of response and abort messages | TCAP messages of these types specify Òroute on global titleÓ in the SCCP Called Party Address. |
| M | Point code, SSN internetwork addressing of response and abort messages | TCAP messages of these types specify Òroute on point code + SSNÓ in the SCCP Called Party Address |
| M | Q ASE invoker of infoAnalyzed | The Q ASE invokes the infoAnalyzed operation in order to obtain an NRN. |
| M | endUserNumber parameter present in analyzeRoute | The endUserNumber parameter, although optional in the underlying (AIN) protocol is mandatory for NP QueryÐResponse. It contains the portable number for which the corresponding NRN is required. |

Table 3(continued) Q Application Service Element Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| M | Q ASE performer of analyzeRoute | The Q ASE performs this operation to extract the NRN from the response message returned by the NP Database. |
| M | networkRoutingNumber present in analyzeRoute | The endUserNumber parameter, although optional in the underlying (AIN) protocol is mandatory for NP QueryÐResponse. It contains the NRN corresponding to the portable number. |
| V | min( Tq ) | Interval between initial query and expected response. 3 sec. |

Table 4 DB Application Service Element Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| M | Global title internetwork addressing of query messages | TCAP messages of this type specify Òroute on global titleÓ in the SCCP Called Party Address. |
| N/A | Point code, SSN internetwork addressing of query messages | TCAP messages of this type specify Òroute on point code + SSNÓ in the SCCP Called Party Address |
| N/A | Global title internetwork addressing of response and abort messages | TCAP messages of these types specify Òroute on global titleÓ in the SCCP Called Party Address. |

Table 4(continued) DB Application Service Element Protocol Capabilities

| Status | Description | Comments |
| --- | --- | --- |
| M | Point code, SSN internetwork addressing of response and abort messages | TCAP messages of these types specify Òroute on point code + SSNÓ in the SCCP Called Party Address |
| M | DB ASE performer of infoAnalyzed | The DB ASE performs the infoAnalyzed operation, determining an NRN corresponding to the endUserNumber parameter. |
| M | endUserNumber parameter present in analyzeRoute | The endUserNumber parameter, although optional in the underlying (AIN) protocol is mandatory for NP QueryÐResponse. It contains the portable number for which the corresponding NRN is required. |
| M | DB ASE invoker of analyzeRoute | The DB ASE invokes this operation to transfer the NRN to the Q ASE. |
| M | networkRoutingNumber present in analyzeRoute | The networkRoutingNumber parameter, although optional in the underlying (AIN) protocol is mandatory for NP QueryÐResponse. It contains the NRN corresponding to the portable number. |

References

American National Standards Institute

ANS for Telecommunications—Signalling System Number 7 (SS7)—Call Completion to a Portable Number ANSI T1.660–1997	2, 3, 9

ANS for Telecommunications—Signalling System Number 7 (SS7)—Message Transfer Part ANSI T1.111–1996	3

ANS for Telecommunications—Signalling System Number 7 (SS7)—Signalling Connection Control Part ANSI T1.112–1996	passim

ANS for Telecommunications—Signalling System Number 7 (SS7)—Transaction Capabilities ANSI T1.114–1996	3

CRTC Interconnection Steering Committee

Network–to–Network Technical Interface for Local Interconnection: Basic SS7 Call Control	3, 4

Acronyms

ANS	American National Standard

ASE	Application Service Element

CLEC	Competitive LEC

CLI	Calling Line Identification

CLIR	Calling Line Identification Restriction

ISUP	ISDN User Part (of SS7)

ILEC	Incumbent LEC

LEC	Local Exchange Carrier

LRN	Location Routing Number (synonymous with NRN)

MTP	Message Transfer Part (of SS7)

NP	Number Portability

NRN	Network Routing Number (synonymous with LRN)

SCCP	Signalling Connection Control Part (of SS7)

SPOI	Signalling Point of Interconnection

SS7	(Common Channel) Signalling System Number 7

SSN	SubÐsystem number, a component of an SCCP address.

TCAP	Transaction Capabilities Application Part (of SS7)

UDT	Unit Data message (of SCCP)

UDTS	Unit Data Status message (of SCCP)

XUDT	Extended Unit Data message (of SCCP)

XUDTS	Extended Unit Data Status message (of SCCP)

# Footnotes

That is, bit 7 of the Address Indicator field is set to 0. See T1.112.3, ¤3.4.1

That is, bit 7 of the Address Indicator field is set to 1. See T1.112.3, ¤3.4.1

That is, bit 7 of the Address Indicator field is set to 0. See T1.112.3, ¤3.4.1

That is, bit 7 of the Address Indicator field is set to 1. See T1.112.3, ¤3.4.1